## Slide 1: acatech – NATIONAL ACADEMY OF SCIENCE AND TECHNOLOGY Smart Hybrid Energy Grids for Smart Regions Prof. Dr. Sebastian Lehnhoff – acatech Project Group „Hybrid Energy Grids“ OFFIS – Institute for Information Technology R&D Division Energy Munich, September 11th, 2013

## Slide 2: Energy Supply Challenges Smart Grids, Smart Cities, Smart Regions
Increasing energy feed-in from volatile decentralized sources
  Increase in storage and transportation requirements
Flexibilization of power demand and supply (Smart Grids)
  Timely (and regionally) coupling of demand/supply processes
Multi-domain flexibilization in Smart Cities  Smart Regions
  Coupling of infrastructures (power/gas/heat/transportation)
  Adequate coupling of processes?
acatech project group „Hybrid Energy Grids“
  30 representatives from industry, government and R&D
  Technical Report „Hybrid Energy Grid for the Energy Turnaround – ICT-Challenges“
Modeling of multi-domain process coupling…

## Slide 3: Power-to-Gas(-to-Power) Process Coupling
Virtual Gas Storage
Flexibilization of hybrid Processes
Flexibilization of hybrid Processes
Electrification of Compressor Stations
Power Generation
Power Consumption
Gas Consumption
Gas Feed-in
Flexible
Generation
Flexible
Consumption
Storage
Flexible
Consumption
Storage
Flexible
Generation
DSM/DR
V2G
VPP
G-DSM
VGS
Gas Generation
CH4/H2
Electricity Conversion
GCC/CHP/Fuel Cell
Transportation
Transportation
Notes: Value Chain
GCC_ Gas combined cycle (GuD-Prozess)

## Slide 4: Multi-Domain Process Coupling Increase in Degrees of Freedom
Smart Cities: integration of power-, gas-, heat- and transportation-systems
Number of 1-dimensional process couplings
  3 Domains: 3
  4 Domains: 6
Multi-dimensional process couplings
Flexible
Generation
Flexible
Consumption
Storage
Flexible
Consumption
Storage
Flexible
Generation
Power
Gas
Flexible
Generation
Flexible
consumption
Storage
Flexible
Consumption
Storage
Flexible
Generation
Heat
Power
Flexible
Generation
Flexible
Consumption
Storage
Flexible
Consumption
Storage
Flexible
Generation
Gas
Heat
Minimization of process distances in hybrid energy systems utilizing Smart Grid methods, complementary methods in gas/heat/transportation-systems, process coupling...

## Slide 5: Multi-Domain Process Coupling Timely differentiated Availabilities in Smart Regions
Utilizing regional alternatives for fulfilling energy demands
E.g.: heat can be produced from solar/electric energy or by combustion (biomass/gas)
  Timely differentiated “process costs”
Where energy infrastructures overlap process coupling is possible
  Conversion processes
  „Bivalent consumers“
Energy demand fluctuates over time
  and space!
  Spontaneous switching between energy sources and infrastructures
Automated solutions required!

## Slide 6: Multi-Domain Process Optimization Beware of complexity trap
Quelle: OFFIS
Quelle: TU Braunschweig
Design challenges:
Where do existing infrastructures support process coupling?
Where is the biggest potential for process coupling?
Operational challenges:
Conversion processes
Automation of process couplings (e.g. bivalent consumers)
Timely and spatially flexibilization along the
  Power(-to-{Gas;Heat;Mobility;Power})* process chain
fragmented, single-purpose, heterogeneous ICT
Inhomogeneous systems (high integration costs)
(High-)potential options for flexibilization will not be considered
Missing incentives for development/hybridization!
Beware of complexity trap! [FEG2012]

## Slide 7: Integrated Energy Information Systems Overall System Optimization
Generation
Transmission
Distribution
DER
Customer Premise
Process
Field
Station
Operation
Enterprise
Market
Domains
Zones
Component
Layer
Protocol
Protocol
Communication Layer
Data Model
Data Model
Information Layer
Function Layer
Outline of Usecase
Subfunctions
Quelle: M/490 Reference Architecture WG,
CEN-CENELEC-ETSI, 2011
Business Layer
Business Objectives Polit. / Regulat. Framework
Established ICT-concepts:
  Decentralization/hierarchies
  Reference architectures/models
Adequate design of the ICT-infrastructure
necessary
  Data exchange platform
  „Internet of Energy“
Standards for communication and automation
  Definition of profiles
  Tool development and support
  Security!

## Slide 8: Regulation Framework for Hybrid Energy Grids
Timely and spatially differentiation of coupling and storage processes
Identification of „relevant“ domains
  Storage and transport capacities (timely and spatially differentiable)
  Comprehensive area-wide infrastructure
  Decentralized (bidirectional/two-way) access
Energy systems in Germany (ordered by total end user consumption)
  Mineral oil
  Gas
  Power
  Heat
PAPER HYBRID ENERGY GRIDS

## Slide 9: Regulation Framework for Hybrid Energy Grids (cont‘d)

## Slide 10: Evaluation of Process Chains in Hybrid Energy Grids
Identification of promising business/use cases
Additional energy sectors/domains?
  What about mobility/public transportiation?
Alternative (more efficient) coupling processes?
  „Virtual“ coupling processes
  Compressor stations
  Thermal industrial (melting) processes
  Multivalent coupling processes (data centers, Smart City concepts etc.)
Power-to-Gas-to-Heat
„more electric power, less gas“ (and vice versa)

## Slide 11: Virtual Coupling into the Mobility Domain
Multivalent, highly available coupling process
But: coupling process is „refueling“ not „driving“
  Tightly knitted, public/private stations/charging points
  Coupling of power and gas grid via (gas) filling stations
Timely and spatially flexibilization of domain specific energy consumptions
  Timely differentiable, dynamic pricing of fuels
  Dense public/private stations/charging points

## Slide 12: Hybrid Energy Grids for Smart Regions and the Energy Turnaround
Hybrid energy grids exhibit a highly increased complexity compared to “conventional” Smart Grids
  Power, gas und (district) heating, supply systems for fuels
Automated operation only feasible with integrated ICT-concepts
  „Energy information systems with distributed intelligence“
Design/optimization: regional approaches
  Energy supply and demand fluctuate over time and space!
Identify adequate/efficient system architectures
Highlight migration paths
http://www.acatech.de/publikationen-hybridnetze
S. Lehnhoff, S. Rohjans, H.-J. Appelrath: ICT-Challenges in Load Balancing across Multi-Domain Hybrid Energy Infrastructures. In: it – Information Technology, 2/2013, ISSN 1611-2776.
http://www.acatech.de/publikationen-hybridnetze

## Slide 13: Data Center as Multivalent Process Coupler Smart City-Component
Gas
Gas
Heat
Data Center
(Source: servermaniac.de)
Power
Heat
Data center as energy conversion process:
  Power-to-Heat: „very efficient heater with its own cooling system“
  Large amounts of waste heat dependent on the cooling concept
  Power grid connection point dimensioned for the maximum projected ICT-performance
  Increasing energy density
Heating Plant
Heat
Municipal
Heat Consumption
Heat

## Slide 14
PV
PV
WW Heat
el. Power
Heat
el. Power
Gas
Cold
Gas
(Pressure)
el. Power
el. Power
Heat
el. Power (1 MW)
Animal Feed Drying
Various heat-levels
(heat pumps on site)
Sewage Plant
(CHPP on site)
Data Center
Gas Expansion Site
Waste Water Heat
(1,9 MW)
Oldenburg, Germany, 2013
Heat
el. Power
Cold
el. Power
Gas
Heat
Notes: Starting from a energetic/thermal model of data centers we went looking for adequate configurations/constellations

## Slide 15
Thank you! Prof. Dr. Sebastian Lehnhoff R&D Division Energy lehnhoff@offis.de